Tunable non-linear response in 2D materials
Claudio Attaccalite
CNRS/CINaM, Aix-Marseille Universite (FR)

---
Outline:
Introduction to non-linear response
Tunable second harmonic generation
Sum-frequency generation
    and pump-probe

---
Non-linear optics
First experiments
on linear-optics
by P. Franken 1961
P(r,t) = color red {%chi^{(1)} E }+ color blue { %chi^{(2)} E^2 + %chi^{(3)} E^3 + O(E^4) }
Linear optics
Non-linear optics
[Speaker Notes: La DFT nous donne un hamiltonien de départ que j'utiliserai ensuite pour calculer les propriétés qui nous intéressent]

---
Real-time approach 1/3
ℱ𝒯
Quasi-monochromatic-field
ℱ𝒯
Different response functions can be calculated with the same Eqs.
Results analysis is more difficult
Quasi-monochromatic-field

---
Real-time approach 2/3
ℱ𝒯
H^{eff} ={color green h^0_{bold k}} + {color blue {%DELTA h_{bold k}}} + {color magenta { V_{bold H} [ %DELTA %rho ]}} + {color red {%SIGMA_{sex} [ %DELTA %igamma ] } }

---
Real-time approach 2/3
Real-time polarization
Model

---
Design materials for non-linear optics
with ab-initio codes
Lithium niobate
Nonlinear optical response of ferroelectric oxides
Phys. Rev. Mat. 6 (6), 065202 (2022)
Synthesis
Properties
Design
Tetraphenyl Tetrel
Molecular Crystals
New molecular crystals with non-linear response comparable to LiNbO3 J. Phys. Chem. C, 126, 7, 3713–3726(2022)

---
Tunable non-linear response in 2D materials

---
Gated 2D material

---
Gated 2D material

---
SHG with gate electric field

---
SHG with gate electric field

---
SHG with gate electric field
?

---
How to calculate the ionic/electronic contributions
Electronic contributions
(fixed ions – with E field)

---
How to calculate the ionic/electronic contributions
Electronic contributions
(fixed ions – with E field)
Ionic contributions
(relaxed ions - no E field)

---
Ionic vs Electronic contribution

---
Theory and experiments

---
Theory and experiments
"Electric-field switchable second-harmonic generation in bilayer MoS2 by inversion symmetry breaking."
lein, Julian, et al. , Nano letters 17, 392 (2017)

---
Sum Frequency Generation

---
Efficient light conversion
"Dual resonant sum frequency generations from two-dimensional materials."
Kim, Youngjae, et al. Nano letters 20.6 (2020): 4530-4536.

---
How to simulate P&P ?

---
Non-linear response with more than one field

---
Use square root fitting

---
We do not need to sample
fundamental period !!

---
SFG and DFG

---
Sum frequency generation (hBN)

---
Diff. frequency generation (hBN)

---
MoS2 is even more beautiful

---
MoS2 is even more beautiful
 Difference frequency generation in monolayer MoS2
Wang, Y.,et al.
Nanoscale, 12(38), 19638-19643 (2020).

---
ThZ induced SHG

---
ThZ induced SHG
Terahertz-field-induced second-harmonic generation in a beta barium borate crystal and its application in terahertz detection, Handa T. et al. APL 95(1) (2009), doi:10.1063/1.3176439.
Terahertz emission from giant optical rectification in a van der Waals material,
Handa, Taketo, et al. " Nature Materials (2025): 1-6.

---
Conclusions
Tunable non-linear response in 2D materials by static or ThZ electric field
We can simulate sum/difference frequency generation with short similation time
References
Sum frequency generation from real-time simulations in two-dimensional crystals
MN. Pionteck, M. Grüning, S. Sanna, C. Attaccalite
arXiv preprint arXiv:2503.07095 (2025)
Tunable second harmonic generation in 2D materials: comparison of different strategies
S Grillo, E. Cannuccia, M Palummo, O Pulci, C Attaccalite
SciPost Physics Core 7 (4), 081 (2024)
Mike N. Pionteck
Justus Liebig University
Gissen
Simone Grillo
Max Planck Hamburg
Simone Sanna group
Justus Liebig University Giessen
Myrta Grüning
Queen’s Univesity

---
Tuning SHG with doping